## Slide 1: All Grain Brewing
Brief Introduction

## Slide 2: Overview
Starches are broken down into sugars which are fed to a small colony of yeast.
The yeast colony grows, consumes sugars producing carbon dioxide and alcohol
After some time (~ 2 weeks for ales and ~4-6 weeks for lagers) fermentation ceases
Mixture is considered beer at this point.
Carbonated and bottled
Consumed

## Slide 3: Barley
Dry malt extract packaged and sold
  -Good for homebrewers who want to make a good beer with least hassle
  -Allows for consistency
Semi-Raw Form
  -More advanced brewing
  -Allows greater manipulation of sugar profiles and beer flavor

## Slide 4: Wort
What is it? How do you make it?
Barley is crushed with a mill
  Husk breakage to optimize starch availability
    Too thin = porridge
    Too thick = thin bodied beer
  Steeped in water to extract starches and create wort (Mashing)

## Slide 5: Mashing (Creating Wort)
Starches given, sugars needed
  Enzymes are found naturally in grain
    Generate needed fermentable sugars from starches (saccharification)
  Incremental Heat Stages
    Strike Water
    Infuse grains with hot water, rests, & mash out (170 F)
    Lautering: Recirculating - Sparging
      Wort is extracted from grain

## Slide 6: Enzymes
Enzyme | Optimum Temperature Range | Working pH Range | Function
Phytase | 86-126°F | 5.0-5.5 | Lowers the mash pH. No longer used.
Debranching (var.) | 95-113°F | 5.0-5.8 | Solubilization of starches.
Beta Glucanase | 95-113°F | 4.5-5.5 | Best gum breaking rest.
Peptidase | 113-131°F | 4.6-5.3 | Produces Free Amino Nitrogen (FAN).
Protease | 113-131°F | 4.6-5.3 | Breaks up large proteins that form haze.
Beta Amylase | 131-150°F | 5.0-5.5 | Produces maltose.
Alpha Amylase | 154-162°F | 5.3-5.7 | Produces a variety of sugars, including maltose.
Major Enzyme Groups and Functions

## Slide 7: Lautering
Liquid/Solid separation to get wort
Water temp @ 170 F
Recirculation
  Initial few quarts are “dirty”
  Repeat if grain bed is disturbed or wort is cloudy
Sparging
  Rinsing of grains, this is the wort, collect in brewing pot

## Slide 8: Hopping
Bring kettle to the burner, bring to a boil
Add hops, boil for an hour
  Isomerize Hop Oils
  Sanitation
Hopping Schedules
  Bittering
  Aromatic/Flavoring

## Slide 9: Hops
AAU’s = [Oz] * [Alpha Acid %]
Bittering – @60 minutes
Aromatic/Flavoring – @15-10 Minutes
Dry Hopping – Hopping in fermenter

## Slide 10: Yeast
Attenuation – Percentage of sugars converted
Flocculation – How fast or well yeast cells clump and sink
Lag Time – Time between initial pitch and vigorous bubbling from air lock

## Slide 11: Yeast (cont)
Ale – Top fermenting (55-70 F)
Lager – Bottom fermenting (40-50 F)
Dry – Dehydrated, easy to use, need rehydration
Liquid – More varieties in vials, different flavors

## Slide 12: Fermentation
5 Gallon batches, standard size
Ales – 2 weeks
Lagers – 4 Weeks
Secondary Fermentation

## Slide 13: Bottling
12 – Oz standard
Carbonation – Transfer beer to bottling bucket, add priming sugar
Bottle and Cap – Two weeks minimum, Conditioning

## Slide 14: Laboratory Info
First Half:
  All-Grain Wort Design and Optimization
  Scale Down 5-Gal Batch to 1 Liter
  Determine the affects of…
    Mash Rest Temperature
    Mash Rest Duration
  …on starch to sugar Conversion
Second Half
  Take results from 1st half of semester and ferment to the final product.

## Slide 15: Sugars
Glucose - Fermentable
Maltose - Fermentable
Maltotriose – Semi-Fermentable
Maltotetraose - Unfermentable
Dextrins - Unfermentable
Starch - Unfermentable